## Slide 1: Open Networking?
Open Hardware
ONIE
APD

## Slide 2: Open Networking: What is It?
Is it?
  Linux Foundation
  ONF
  SDN
  Openflow
  API
Or is it?
  Freedom
  Choice
  Flexibility
  Community

## Slide 3: Open Networking: Why do I care?
Operational Flexibility
Innovate Faster
Control your back office destiny
Simple
Did I mention Cost?

## Slide 4: Open Hardware

## Slide 5: Open Networking: “Whitebox switch”

## Slide 6: Industry-Standard Network Hardware
QFX 3500
Nexus 3100
Nexus 9000
7500E
7250X
HCL:
Agema, Dell Edge-Core, HPE, Mellanox, Penguin Computing,
Quanta, Supermicro
powered by
Juniper
Cisco
Arista
Brite-Box | White Box
* Spectrum not T2
*
Notes: The same merchant silicon powers all vendors today in the data center.

## Slide 7: APD

## Slide 8: ACPI Platform Description (APD)
Operating System
Operating System
ACPI extension for networking
  used for PCs/servers
Cuts Platform integration time
  months to days
Accelerate platform availability
Content Presented Under Embargo Until March 10, 2015 10 AM PT
Standardizing Platform Description
Before
With APD
Platform Specific Driver
Platform Specific Driver
Platform Specific Driver
Description
Description
Description
Generic Platform Driver
Notes: Ease network platform integration, let the hardware vendor control their destiny
Goal: Broader set of devices that people can leverage
With APD, you get a hardware abstraction. OS = keep everything generic. For anything platform specific, keep it in the platform
Disaggregate the model to make it fast to innovate
- Can support all types of architectures and switches
- Code embedded in the bios and we parse the information on the NOS
Cuts the human intervention, all automated
Upstreamed and in 4.4 kernel

## Slide 9: Open ecosystem for open networking to thrive
Switches
Linux Networking Model
Self-described platform to any OS
Load any OS on any platform
Servers
uboot and PXE
SERVER OS
ACPI
NETWORK OS
Notes: Ease network platform integration, let the hardware vendor control their destiny
Goal: Broader set of devices that people can leverage
With APD, you get a hardware abstraction. OS = keep everything generic. For anything platform specific, keep it in the platform
Disaggregate the model to make it fast to innovate
- Can support all types of architectures and switches
- Code embedded in the bios and we parse the information on the NOS
- Cuts the human intervention, all automated

## Slide 10: ACPI
Without ACPI
With ACPI
Steps
0, 1
Test
Ship
Port
ONIE
Port
OS
Port
ONIE
Describe
Platform
Certify
Ship
Standards Based OS Vendor Specific
Notes: green = standards based
stacked = done in parallel by multiple hardware vendors
moves platform description over to the standards based, parallel hardware vendor side
This is a standard practice for servers. Tools are open.
Testing
spread out more
hardware vendors self certify, hopefully catch most of the bugs
OS vendors certify
OS Agnostic

## Slide 11: ONIE

## Slide 12: Open Networking: What’s an ONIE?
“PXE that doesn’t suck”
  Cumulus Networks contribution to OCP
  Enhanced Boot loader of Linux Kernel + BusyBox
  Enables install NOS of your choice
Notes: http://onie.org/about/
https://busybox.net/about.html
BusyBox: The Swiss Army Knife of Embedded Linux
BusyBox combines tiny versions of many common UNIX utilities into a single small executable. It provides replacements for most of the utilities you usually find in GNU fileutils, shellutils, etc. The utilities in BusyBox generally have fewer options than their full-featured GNU cousins; however, the options that are included provide the expected functionality and behave very much like their GNU counterparts. BusyBox provides a fairly complete environment for any small or embedded system.
BusyBox has been written with size-optimization and limited resources in mind. It is also extremely modular so you can easily include or exclude commands (or features) at compile time. This makes it easy to customize your embedded systems. To create a working system, just add some device nodes in /dev, a few configuration files in /etc, and a Linux kernel.

## Slide 13
Just Add Network OS

## Slide 14: Bare No More: The Emperor has Cloths!
LINUX KERNEL
switchd
Routing
Tunneling
Network
Interfaces
Bridging
Netfilters
Industry-Standard Hardware
Switch Silicon
CPU
RAM
Flash
Power
Fan
Front Panel Ports
Hmm… a Server with 32 100G LINE-RATE NIC’s?
Notes: Animation

## Slide 15: Automation
Basics of booting a switch
Ansible Playbooks
Puppet manifests

## Slide 16: ONIE and ZTP – The basics
DHCP Request with ONIE Option
DHCP Address with URL for OS Image
DHCP Request with ZTP Option
DHCP Address with script URL
Pull Puppet/Chef/Ansible Scripts
OS Boots
Baseline Configuration Applied
Device Specific Configuration Applied

## Slide 17: ZTP with DHCP - example dhcp.conf
ddns-update-style none;
default-lease-time 4320;
max-lease-time 8640;
authoritative;
option cumulus-provision-url code 239 = text;
subnet 192.168.0.0 netmask 255.255.255.0 {
range 192.168.0.100 192.168.0.200;
option routers 192.168.0.1;
option domain-name-servers 192.168.0.1;
option domain-name "lab.mycompany.com";
option cumulus-provision-url "http://192.168.0.1/provision.sh";
}

## Slide 18: ZTP Scripts can be Powerful and/or Simple
#!/bin/bash
# Upgrade and install Puppet
apt-get update –y
apt-get upgrade –y
apt-get install puppet –y
echo "Configuring puppet" | wall –n
sed -i /etc/default/puppet -e 's/START=no/START=yes/’
service puppet restart
# CUMULUS-AUTOPROVISIONING
exit 0
#!/bin/bash
mkdir -p /root/.ssh
/usr/bin/wget -O /root/.ssh/authorized_keys http://192.168.0.1/ssh.keys
#CUMULUS-AUTOPROVISIONING

## Slide 19
Infrastructure as code
Enforcement from central location
Easy change control
Configuration Management
Hot Swap the Whole Switch
With automation the whole switch can be replaced and provisioned
High capacity, fine-grained failure domain
Weeks and months now take seconds
Pods of equipment can be stamped out in multiple locations
Rapid Provisioning
NetDevOps: Automation Use Cases
OBM
OBM
OBM
Notes: Once you understand the power of choice and solutions brought about by Cumulus Linux, the next step is to integrate Cumulus Linux into brownfield and greenfield architectures.
IP Fabrics are the most flexible network architectures when it comes to high capacity, scale and evolution.
Enables Scale-out architecture
Easy to configure and troubleshoot
Easy to add new racks
Standard OSPF/BGP – helps with interoperability
Can be used as an underlay in conjunction with Network Virtualization Overlays
Network Virtualization Overlays add additional flexibility
Flexible Virtual Network
Scalable, Multi-tenant
Integrated with Cloud Orchestration tools
Yet, they need a simple migration path coexistent with their existing network architecture
CL2.5 brings the flexibility of L2MLAG network architectures
CL2.5 brings the flexibility of L2MLAG network architectures. Customers can now drop in a networking hardware running Cumulus Linux in existing environments and migrate at their pace and based on the needs to Modern DC networks.
FHRP, Improved Linux-bridging and ifupdown2 integration for required L2 fabrics, L2 scale

## Slide 20
Kick off user customization for new hires
Revoke user permissions as they change job roles
User Administration
Maintenance Tasks
Automate maintenance tasks such as log and space cleanup, patching applications, etc
Shortened change-windows and less down-time
No need to know how to install an App on Linux
Apps can be installed, configured and up and running with one command
Easy Application Deployment
NetDevOps: Automation Use Cases
OBM
OBM
OBM
Notes: Once you understand the power of choice and solutions brought about by Cumulus Linux, the next step is to integrate Cumulus Linux into brownfield and greenfield architectures.
IP Fabrics are the most flexible network architectures when it comes to high capacity, scale and evolution.
Enables Scale-out architecture
Easy to configure and troubleshoot
Easy to add new racks
Standard OSPF/BGP – helps with interoperability
Can be used as an underlay in conjunction with Network Virtualization Overlays
Network Virtualization Overlays add additional flexibility
Flexible Virtual Network
Scalable, Multi-tenant
Integrated with Cloud Orchestration tools
Yet, they need a simple migration path coexistent with their existing network architecture
CL2.5 brings the flexibility of L2MLAG network architectures
CL2.5 brings the flexibility of L2MLAG network architectures. Customers can now drop in a networking hardware running Cumulus Linux in existing environments and migrate at their pace and based on the needs to Modern DC networks.
FHRP, Improved Linux-bridging and ifupdown2 integration for required L2 fabrics, L2 scale

## Slide 21
Deter threats as they happen rather than ‘when’ you notice
Grab logging information and make it easy to see the attack vector
Automatic Threat Response
Hitless Upgrades
Bring switches offline automatically without affecting the network
Check surrounding devices and check route tables to know network state
Bad fan? High Temperature? Don’t just know when it happens but automatically respond
Reactive Network Changes
NetDevOps: Automation Use Cases
OBM
OBM
OBM
Notes: Once you understand the power of choice and solutions brought about by Cumulus Linux, the next step is to integrate Cumulus Linux into brownfield and greenfield architectures.
IP Fabrics are the most flexible network architectures when it comes to high capacity, scale and evolution.
Enables Scale-out architecture
Easy to configure and troubleshoot
Easy to add new racks
Standard OSPF/BGP – helps with interoperability
Can be used as an underlay in conjunction with Network Virtualization Overlays
Network Virtualization Overlays add additional flexibility
Flexible Virtual Network
Scalable, Multi-tenant
Integrated with Cloud Orchestration tools
Yet, they need a simple migration path coexistent with their existing network architecture
CL2.5 brings the flexibility of L2MLAG network architectures
CL2.5 brings the flexibility of L2MLAG network architectures. Customers can now drop in a networking hardware running Cumulus Linux in existing environments and migrate at their pace and based on the needs to Modern DC networks.
FHRP, Improved Linux-bridging and ifupdown2 integration for required L2 fabrics, L2 scale

## Slide 22: Provisioning Playbooks

## Slide 23: Project Tree Troubleshooting

## Slide 24: Infrastructure as Code
Configuration for network nodes is stored:
  Cookbooks
  Manifests
  Playbooks
Revision control tools:
  Git (Stash, Github)
  Subversion
  Mercurial
  Clearcase
  CVS
Where are my configs?

## Slide 25: Pick’em - Automation Tools
Agentless | Agent-based
Requires no additional application software | Requires installation of an application (e.g., a daemon) to communicate with the control server
Relies on existing processes (such as SSH) to communicate with the control server | May also use existing processes to perform its functions
Notes: Speaking Points: Automation tools are either agent-based or agentless.
Agent-based tools require the installation of code on the managed device. This allows two-way communication with the control server (i.e., either the server or client can initiate actions). The agent will consume local system resources to run.
Agentless tools require no additional software to be installed on the managed device. However, without a local component, all actions must be initiated by the control server. The server will rely on other software (such as SSH) to communicate with the managed device.

## Slide 26: Want to learn more?
Community
  http://community.cumulusnetworks.com/
Slack Channel
cumulusnetworks.slack.com
Download Cumulus VM’s
https://cumulusnetworks.com/cumulus-vx/
Demo’s and Lab’s: https://support.cumulusnetworks.com/hc/en-us/articles/201787686 https://support.cumulusnetworks.com/hc/en-us/sections/200398866